CisteraScreenCapture

CisteraScreenCapture consists of a windows service (CisteraScreenCaptureService) and admin UI (CisteraScreenCaptureUI)
Both applications write logs.

Platform: Windows7+, C#4.5

Installing and running
Launch CisteraScreenCaptureSetup.msi. It will install both CisteraScreenCaptureService and CisteraScreenCaptureUI and automatically launch them upon successful installation.
The systray icon changes corresponding to status of the service. It is normal when the service runs and inverted when it is stopped.
Any problem should be traced in logs which can be open by clicking Logs in the systray menu.

Uninstalling
Run CisteraScreenCaptureSetup.msi. It will stop CisteraScreenCaptureService and CisteraScreenCaptureUI if they are running and uninstall them.

CisteraScreenCaptureUI
It displays a systray icon.

While CisteraScreenCaptureService runs independently on user sessions, CisteraScreenCaptureUI is auto-started for every user logged in and establishes connection to the service.

Editing and managing the service is possible only with administrator privileges.

Systray menu items
- Settings (parameters for CisteraScreenCaptureService)
- Run (start/stop CisteraScreenCaptureService)
- Silently (when checked, toast messages are suppressed)
- Logs (both processes write own logs which can be helpful application diagnostic)
- Exit (quit CisteraScreenCaptureUI while CisteraScreenCaptureService remains untouched)

CisteraScreenCaptureService
CisteraScreenCaptureService runs permanently and monitors user login/logoff/unlock/lock events, where unlock/lock are treated like login/logoff. When user login/unlock happened, CisteraScreenCaptureService uses mDNS discovery to try to resolve the service name.

Then CisteraScreenCaptureService sends HTTP GET request:
 <ip received by mDNS response, otherwise a default preset ip>/screenCapture/register?username=<user name of logged in user>&ipaddress=<ip of client>&port=<client's port which is listening to server>

Also CisteraScreenCaptureService starts accepting TCP connections from Server which are used to exchange with messages. So, Server anytime after can send to CisteraScreenCaptureService a command to launch/stop ffmpeg streaming.

Tcp connection is kept alive since it was created by Server and until it is purposely closed by either of the sides.
When tcp connection is closed by any side, CisteraScreenCaptureService stops ffmpeg stream (if any).
If tcp connection is closed/broken by Server, CisteraScreenCaptureService proceeds listening for new connections from Server until the current user is logged off. When the user is logged off, CisteraScreenCaptureService stops accepting tcp connections.
CisteraScreenCaptureService closes tcp connection (if any) only when the current user is logged off. This way Server is notified that the session is over (either the user is logged off or network is broken).

Ffmpeg is running under SYSTEM account like CisteraScreenCaptureService itself so cannot be impacted by a non-administrator user. If ffmpeg exited for any reason while the user is not logged off (was killed by an administrator or died due to a system error), CisteraScreenCaptureService keeps restarting it.

General message format for communicating between CisteraScreenCaptureService and Server:
request/response:
[message name+body length (2 bytes)][message name (ASCII string terminated with '\0')][message body, which is interpreted respectively to the message name]

Every request must get a response before sending next request. Responses have the same format as requests.

Messages:
direction	description	name	request body	response body
server -> CisteraScreenCaptureService	The server turns on SSL on this TCP channel after receiving a success response. The server is SSL server. / The client turns on SSL after sending a success response. The client is SSL client and initiates SSL handshake.	SslStart	nothing (0 bytes)	OK or error message (ASCII string terminated with '\0')
server -> CisteraScreenCaptureService	Launch ffmpeg stream to the server. If such a stream is running already, it will be terminated and a new one launched.	FfmpegStart	ffmpeg parameters string excluding ffmpeg itself (ASCII string terminated with '\0') / Comment: / The source of captured video (usually name of display but not only) is configurable on the client and thus should not be sent by the server. As ffmpeg arguments should go in certain order, the client will look for -framerate in the string sent by the server and insert display parameters just after it.	OK or error message (ASCII string terminated with '\0')
server -> CisteraScreenCaptureService	Stop ffmpeg.	FfmpegStop	nothing (0 bytes)	OK or error message (ASCII string terminated with '\0')
server -> CisteraScreenCaptureService	Polling to keep connection alive.	Poll	nothing (0 bytes)	OK or error message (ASCII string terminated with '\0') / Error can be anything that happened since previous message from Server (e.g. ffmpeg got broken).